## Slide 1
WWW.FLOWSERVE.COM
Commercial / Technical Presentation
NEW Worcester 51/52 Series
James Howard
Training Presentation

## Slide 2: Flowserve at a Glance
~16,000 Employees
Over 50 Leading Product Brands
10,000+ Customers Annually
163 Aftermarket QRCs (Quick Response Centers)
5,000,000+ Assets (Installed Base)
Over 50 Countries

## Slide 3: Global Reach and Local Presence
GLOBAL REACH
AND LOCAL PRESENCE
Flowserve people, processes and experience are keys to providing critical local support for customers in more than 50 countries. Flowserve has 180 quick response centers and 75 manufacturing facilities across the world.
World Headquarters
Sales Offices
Service Centers & Quick Response Centers
Manufacturing Plants & Regional Operations Centers
*Excludes non-consolidated Joint Venture operations

## Slide 4
Lorem Ipsum is simply dummy text
Worcester 51/52 Revitalized
Globally Focused Product – One product design which meets the standards and certifications required to compete in all global markets
Market Driven Product Certifications - This product meets the latest editions of globally desired product certifications to support existing and future customer expectations, e.g., API 607, API 641, ISO 15848, API 608 & ISO 17292
Improved Availability - Globalized strategy and product consistency will support shorter lead-times in our new 51/52 series products
Enhanced safety - Elimination of the setscrew retained end plug, preventing end plug blow-out
Commercial Improvements - Commercial improvements achieved with global sourcing and rationalized design

## Slide 5: Worcester 51/52 Features and Benefits
Live Loaded Packing – Engineered Belleville washers provide continued packing performance to fugitive emissions standards
Locking Clip – Maintains gland nut for actuated applications ensuring stem seal performance, does not have to be changed for actuation
PTFE Body Seals – Firesafe compliant with PTFE body seals. Maintains robust compliance to fugitive emissions standards.
Secondary Stem Seal – PTFE sealing ring (optional O-ring available), ensures packing performance and continued emissions compliance
PTFE Bearing – Designed to eliminate accelerated wear of graphite from rotating gland during cycling applications

## Slide 6: Worcester 51/52 Features and Benefits
Lorem Ipsum is simply dummy text
Duplex stem as standard- provides a greater yield safety factor and higher MAST when compared to standard 316 Stainless Steel and complies with API 608 & ISO 17292
Threaded Insert- Provides a safe & simple method of retaining the valve contents and eliminated extra leak paths and risks associated with using retaining screws
Dual Certified Carbon Steel Materials- Cast Carbon Steel material is dual certified as LCB/LCC for low temperatures and corrosion resistance
Impact Tested as standard:
Required materials are impact tested to comply with PED requirements as standard at their expected minimum operating temperatures:
CF8M impact tested at -196°C (-320.8°F)
LCB/LCC impact tested at -46°C (-50.8°F)
Duplex impact tested at -50°C (-60°F)
Robust Drivetrain- Enlarged stem to ball connection provides enhanced reliability and service longevity

## Slide 7: Worcester 51/52 Features and Benefits
Seat Design – Available in a wide range of materials, and are cavity pressure relieving (CPR) design as standard
Anti-Static – Anti-static stem to body connection as standard, no longer an “add on” feature
Actuation – ISO 5211 and Shell MESC SPE 77-300 compliant for ease of automation
Stem Finish – 32Ra surface finish on stem sealing areas further improve packing longevity

## Slide 8
Lorem Ipsum is simply dummy text
Existing design
New design
Existing design
51/52 - DN15 to DN50 (0.5” to 2”)
51/52 – DN80 to DN200 (3” to 8”)
Worcester 51/52 Stem Sealing Comparison
NOTES:
O-rings are optional and not included as standard stem build
Depending on the valve size and series, the stem assembly build is slightly different due to space constraints
New 51/52 series valves will not use the same repair kits as the existing 51/52 series
Metal Gland
Thrust Bearing
Graphite Packing
Disc Springs
Belleville Washers
Metal Gland
PTFE Bearing
New design
‘O’ Ring
Thrust Bearing
‘O’ Ring Retainer
Graphite Packing
Graphite Packing
Metal Gland
‘O’ Ring
Belleville Washers
PTFE Bearing
Graphite Packing
Metal Gland
Thrust Bearing
Stem Location Ring
Stem Location Ring
Thrust Bearing
Secondary Stem Seal
Green highlights new features

## Slide 9
Lorem Ipsum is simply dummy text
Worcester 51/52 P/T Chart
Group 1.2 represents dual certified LCB/LCC and WCB/WCC | Group 2.2 represents CF8M

## Slide 10
Worcester 51/52 Seat Materials

## Slide 11: Worcester 51/52 Technical Details
Lorem Ipsum is simply dummy text

## Slide 12: Worcester 51/52 Materials
Lorem Ipsum is simply dummy text

## Slide 13: Worcester 51/52 Materials
Lorem Ipsum is simply dummy text
DN150 (6”) and DN200 (8”) standard with gear

## Slide 14: Worcester 51/52 Torques and MAST
Lorem Ipsum is simply dummy text

## Slide 15: Worcester 51/52 FMK Models
Lorem Ipsum is simply dummy text
Mounting dimensions are outlined in product brochure for FMK creation when not using Worcester brackets and actuators

## Slide 16: Worcester 51/52 Updated Product Coding
Lorem Ipsum is simply dummy text

## Slide 17: Worcester 51/52 Site Manufacturing and Availability
Lorem Ipsum is simply dummy text
MM Nagar, India
DN15 – DN 200 (1/2” – 8”)
Class 150 / 300
Carbon and Stainless Steel
Seats: PTFE / RTFE / Fluorofill/Polyfill
Delivery (Ex Works):
Projects: 16-18 weeks
MRO: 12 weeks
Consult MMN ComOps for other materials
Cookeville, TN USA
DN15 – DN 200 (1/2” – 8”)
Class 150 / 300
Carbon and Stainless Steel
Seats: PTFE / RTFE / Fluorofill/Polyfill
Specials and Engineered to Order Configurations
Delivery (Ex Works):
Projects: 20 weeks
MRO: 6-8 weeks beginning in June 2023
Consult Cookeville ComOps for other materials
Haywards Heath, UK
DN15 – DN 200 (1/2” – 8”)
Class 150 / 300
Carbon and Stainless Steel
Seats: PTFE / RTFE / Fluorofill/Polyfill
Specials and Engineered to Order Configurations
Delivery (Ex Works):
Projects: 20 weeks
MRO: 6-8 weeks beginning in April 2023
Consult Haywards Heath ComOps for other materials

## Slide 18: Worcester 51/52 Applications / Industries
Lorem Ipsum is simply dummy text
Applications/Industries:
Chemical processing
  Thermal fluids
  Oxygen services
  Ammonia
  Chlorine
  Hydrogen peroxide
  Phosgene
Petrochemicals
  BTX
  Ethylene
  Polyolefins/aromatics
Energy
  Gasification
  Hydrogen
  Liquefied natural gas (LNG)
  Steam
Other industries
  Defense / Aerospace
  Food and beverage
  Industrial gases
  Pharmaceuticals
  Water
These are only a few, the application opportunities are
vast for flanged ball valves with global certifications and
enhanced features that are contained in the
re-engineered 51/52

## Slide 19
Lorem Ipsum is simply dummy text
Worcester 51/52 Closing Takeaways
  Highlights:
    Compliant to the most recent editions of globally recognized & accepted product certifications
    Standardized product coding - Identical product coding regardless of global location
    Firesafe design and configuration as standard offering
    Special Configurations, engineered solutions and other alloys available
    Live-loaded stem packing as standard offering
    Stronger duplex stem as standard material offering
    Valves compliant and certified to Shell DVT requirements
    Optional O-Ring Stem Sealing
    Threaded end plug as standard
    Locking handles standard on all sizes up to 4” / Gear standard on 6” and 8”

## Slide 20: Worcester 51/52 Support Contacts
Lorem Ipsum is simply dummy text
Lorem Ipsum is simply dummy text
Worcester 51/52 Reduced Port Flanged Ball Valve
Thank you for your time!
Cookeville Operations: CVOSales@flowserve.com
Haywards Heath Operations: customerservicefcd@flowserve.com
  Global Product Leader: Dadillon@flowserve.com